## Slide 1: Enhancing Robotic Task Prediction with Multi-Modal Inputs: Integrating Voice Commands and Mechanical Measurements
Will Li, Robotic Learning Fall 2024

## Slide 2: Background and Motivation
Conventional, mechanical based robotic control
  High precision
  Limitation: complex interface, accessibility
Multi-modal input
  Flexible, intuitive
  Question: Is it possible for multi-modal input to achieve comparable task performances

## Slide 3: Methods
Problem contextualization
  How much information is needed for robots to ‘learn’ what kind of task is performed?
  Predict task category based on input variables
Experimental conditions
  Rich Mechanical Input vs. Reduced Mechanical Input vs. Reduced Mechanical Input + Multimodal Input
  Compare task classification accuracies
Hypothesis: Reduced mechanical input can be compensated by multi-modal input

## Slide 4: Dataset & Data Preprocessing
RH20T
  Detailed robotic manipulation time-series data
  Over 200 different tasks
Three models compared:
  Baseline – original mechanical input
  Reduced mechanical input – low-pass filtered
  Multimodal – augmented with voice command embeddings.
1D CNN classifier to predict task category

## Slide 5: Results
Model Performances
Statistical Significance with Paired t-test:
  Multi-Modal classifier outperforms Reduced Input classifier significantly.
  Comparable to baseline model

## Slide 6: Discussion
Key takeaway:
  Voice commands as effective alternative modality in robotic control
  Multi-modal input can
    reduce reliance on precise mechanical measurements
    while achieve comparable accuracy
Future Work
  Incorporate real-time human voice commands
  Explore additional modalities

## Slide 7: Thank you!